## Slide 1: Future Very Narrowband Radio Requirements
Implications for the
Hydrologic Warning Community
Timothy J. Salo
Salo IT Solutions, Inc.
May 11, 2011

## Slide 2: Very Narrowband Implications
Topics
Narrowband Mandate and Status
Future Very Narrowband Mandate
Very Narrowband Standards
Very Narrowband Equipment
Testbed Status

## Slide 3: Narrowband Mandate
Narrowband Mandate
Most Part 90 licensees must migrate to 12.5 kHz channel bandwidth by January 1, 2013
Culmination of a very long process
  1995: Original narrowbanding rules adopted
  1997: 12.5 kHz equipment available
  2004: 2013 deadline announced

## Slide 4: Narrowband Mandate
Narrowband Status
FCC appears concerned many licensees haven’t yet migrated
FCC January 26, 2011 Narrowband Workshop
  Lots of interesting info
  Many licensees haven’t migrated yet
  Many haven’t updated licenses
  Funding a concern for many

## Slide 5: Narrowband Mandate
Narrowband Status
What if my cousin doesn’t migrate?
  Waivers will be very difficult to obtain
  FCC public answer:
    Your system will not be incompliance
    You won’t be legally protected from interference
    You may cause interference to lawful systems
    Someone might complain
    Enforcement is another division…
  Alleged private answer
    FCC will cancel wideband licenses

## Slide 6: Narrowband Mandate
Narrowband Resources
FCC January 26, 2011 Narrowband Workshop
  <http://www.fcc.gov/pshs/summits/#narrowbanding_workshop>
  <http://www.youtube.com/watch?v=rdV5DC5Kb7o>
FCC Narrowbanding Website
  <http://www.fcc.gov/pshs/public-safety-spectrum/narrowbanding.html>
Yahoo! LMR Narrowbanding Group
  <http://tech.groups.yahoo.com/group/LMR_Narrowbanding/>

## Slide 7: Very Narrowband Mandate
Very narrowband, 6.25 kHz migration will occur, FCC says
  No date set
  FCC will follow usual rule-making processes
  Note: narrowband deadline ~16 years after equipment availability
Equipment certified after January 1, 2013 must support very narrowband (6.25 kHz) operation

## Slide 8: Very Narrowband Standards
Several emerging very narrowband standards
  Many include data specification
dPMR (digital Private Mobile Radio)
DMR (Digital Mobile Radio)
TETRA
P25 (Project 25)

## Slide 9: Very Narrowband Standards
dPMR (digital Private Mobile Radio)
  European 6.25 kHz digital standard
  Includes both a voice mode and a data mode
  Voice products are just starting to become available in Europe
DMR (Digital Mobile Radio)
  European digital standard
  Multiplexes 12.5 kHz channel

## Slide 10: Very Narrowband Standards
TETRA
  European standard
  TDMA
P25 (Project 25)
  American solution for interoperable public safety radios
  Phase 2 under development
  Reported work on data-only mode apparently suspended

## Slide 11: Very Narrowband Equipment
Some very narrowband equipment starting to become available
  Proprietary data radios
  Standards-based voice equipment
    Icom dPMR system
Remember: Equipment certified by FCC after January 1, 2013 must support 6.25 kHz operation

## Slide 12: Testbed Status
900 MHz spread spectrum radio
  Digi (MaxStream) XTend
VHF narrowband radio
  Maxon SD-171E with ACC 513 modem

## Slide 13: Testbed Status
900 MHz spread spectrum radio
Digi International (MaxStream) XTend

## Slide 14: Testbed Status
900 MHz spread spectrum radio
Digi International (MaxStream) XTend
  900 MHz unlicensed operation
  1 watt transmit power
  9,600/115,200 bps
  Claim line-of-sight (LOS) range of 14 - 40 mile
  Includes mesh networking capability

## Slide 15: Testbed Status
900 MHz spread spectrum radio
Similar devices:
  FreeWave FRG2-IOS
  Laird (AeroComm) ConnexLink
All use different, proprietary on-the-air formats
Most ALERT / environmental monitoring vendors resell or experimenting with these radios

## Slide 16: Testbed Status
900 MHz spread spectrum radio
Attempted communications over:
  Five-mile non-LOS urban path
  Seven-mail not-quite-LOS urban path

## Slide 17: Testbed Status
900 MHz spread spectrum radio
7 dbi mobile omni
Laird MA7-7N
20”

## Slide 18: Testbed Status
900 MHz spread spectrum radio
9.2 dbi omni
Comet KP-20
96”

## Slide 19: Testbed Status
900 MHz spread spectrum radio
9 dbi 5-element yagi
Laird YA9-9
20”

## Slide 20: Testbed Status
900 MHz spread spectrum radio
13 dbi 15-element yagi
Laird YA9-13
57”

## Slide 21: Testbed Status
900 MHz spread spectrum radio
Results
  Communications never established over:
    Five-mile non-LOS path
    Seven-mile not-quite-LOS path
  Communications established over shorter paths
Substantial interference with consumer device
Devices have potential in right circumstances
  Not the solution for HWS

## Slide 22: Testbed Status
VHF narrowband radio
Maxon SD-171E radio and ACC-513E modem
  Narrowband (not very narrowband) VHF radio
    SD-171E/ACC-513E certified for narrowband operation
  Inexpensive
    Commercial off-the-shelf (COTS) product
      Benefits from manufacturing economies of scale
    SD-171E radio: $245
    ACC-513E modem: $89

## Slide 23: Testbed Status
VHF narrowband radio
Maxon SD-171E radio and ACC-513E modem
  Interoperates with Midland SD-171 and ACC-513
    Maxon SD-171E appears to be a superior radio
    Midland radio appears to be obsolete/discontinued

## Slide 24: Testbed Status
VHF narrowband radio
Maxon SD-171E

## Slide 25: Testbed Status
VHF narrowband radio
ACC-513E modem

## Slide 26: Testbed Status
VHF narrowband radio
ACC-513E modem
  H8 8-bit microprocessor

## Slide 27: Testbed Status
VHF narrowband radio
ACC-513E modem
  CML Microcircuits CMX589A GMSK modem

## Slide 28: Testbed Status
VHF narrowband radio
ACC-513E modem
  4,800 bps in narrowband operation
  GMSK modulation
  Link layer frame is based on part of MPT 1327 specification
    Sort of documented in ACC-513E service manual
    Is it an open protocol?

## Slide 29: Testbed Status
VHF narrowband radio
Future plans:
  Test and evaluate Maxon SD-171E/ACC-513E
  Demonstrate interoperability with Midland SD-171/ACC-513
    Maybe

## Slide 30: Very Narrowband Observations
A very narrowband mandate is coming
  Someday; probably not this decade
Several emerging standards offer the prospect of interoperable very narrowband data equipment
  Maybe; not today

## Slide 31: Very Narrowband Observations
HWS vendors and operators should make their needs known to data radio vendors
  Standards-based, interoperable very narrow band data radios
    dPMR data-only radio?
    P25 Phase 2 data-only radio?
    ???
Speak with a collective voice

## Slide 32: Acknowledgement / Disclaimer
This work was supported by National Oceanic and Atmospheric Administration (NOAA) National Weather Service (NWS) Office of Climate, Water and Weather Services.
The opinions expressed here are those of the author, and do not necessarily reflect those of any other individual or organization, including those that have funded, are funding, or may in the future fund the author’s employer, Salo IT Solutions, Inc.

## Slide 33: Very Narrowband Implications
?